## Slide 1: Multi-Robot Coordination in Underwater Mothership-Passenger Systems
Nathan L. Butler, candidate for MS in Robotics
Collaborative Robotics and Intelligent Systems (CoRIS) Institute, Oregon State University
Advisor: Dr. Geoff Hollinger
September 10, 2025
NSF Award No.
2322055

## Slide 2
Rising Sea Levels Threaten Coastal Communities
US Geological Survey (2000), Public Domain
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 3: Ocean-Terminating Glaciers are Data-Rich, but Hazardous
Thwaites Glacier
Antarctica
Larter (2022), Geophysical Research Letters
Intro.
Contrib. 1
Contrib. 2
Summary
Notes: Ocean-terminating glaciers are key contributors to sea level rise, as they are melted from both above and below. What are some key challenges that we’d identify for this environment? Narrow, constrained areas, turbulent ocean currents, no surface access.

## Slide 4: Data Collection with Autonomous Underwater Vehicles (AUVs)
MahmoudZadeh & Yazdani (2023), Ocean Engineering
Modasshir et al. (2018), ROBIO
Single-robot coral reef exploration
Multi-robot environmental monitoring
Intro.
Contrib. 1
Contrib. 2
Summary
Notes: These factors prompt the use of AUVs for exploring this environment. AUVs have been used for marine missions before, however the hazards of the under-ice domain prompt the use of a special type of system that mitigates the risk of expensive equipment loss.

## Slide 5: Mothership-Passenger Systems
Mothership
Deploying multi-robot team in marine under-ice environments
Intro.
Contrib. 1
Contrib. 2
Summary
Notes: Here we introduce the Mothership-Passenger system. We note that in this system, there are multiple avenues for coordinating the Passengers.

## Slide 6: Multi-AUV Mission Planning Frameworks
Hybrid coordination
MahmoudZadeh & Yazdani (2023), Ocean Engineering
Benjamin et al. (2010), JFR
Decentralized coordination
Wang et al. (2022), Ocean Engineering
Intro.
Contrib. 1
Contrib. 2
Summary
Centralized coordination
Yan et al. (2020), Ocean Engineering
Notes: Other marine Mothership-Passenger systems have attacked MR coordination in these ways. Typically, initial mission planning with the Mothership followed by decentralized execution with limited adaptation. While acceptable in relatively short-horizon, static environments, long term deployments in dynamic environments requires methods with enhanced Passenger robot agency/responsiveness. This brings us to our gap.

## Slide 7: Research Gap
How can we leverage a Mothership’s global perspective and computational advantages to bolster decentralized Passenger mission planning routines?
Intro.
Contrib. 1
Contrib. 2
Summary
Notes: How can we leverage the high compute and global perspective offered by a Mothership to enhance team coordination in decentralized Passenger autonomy routines?

## Slide 8: Outline
Introduction: Mothership-Passenger systems and underwater multi-robot mission planning
Contribution 1: Hybrid-decentralization for multi-robot orienteering with Mothership-Passenger systems
Contribution 2: Learning-based coordination for passenger robots in complex task domains
Summary: Conclusions, contributions, and future work
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 9: Hybrid Decentralization for Multi-Robot Orienteering with Mothership-Passenger Systems
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 10
Mothership
Multiple robots deploy, completing tasks, and return
T
T
T
T
T
T
T
?
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 11
Mothership
T
T
T
T
T
T
T
T
T
T
?
?
?
?
?
?
?
The Stochastic Multiagent Orienteering Problem
T
Unvisited
(exceeds budget)
Intro.
Contrib. 1
Contrib. 2
Summary
Notes: MOP/SMOP slide

## Slide 12
How can a hybrid centralized-decentralized network topology available in Mothership-Passenger systems be used to solve complex orienteering problems?
Intro.
Contrib. 1
Contrib. 2
Summary
Notes: Gap

## Slide 13
Hybrid Mission Planning
Passenger k
Use up-to-date local observations
Respond quickly to local disturbances
Mothership
Use aggregated global information
Coordinate system-level actions
Observed local data
Locally-informed plans
Received global data
Globally-informed plans
Decentralized Planning
Centralized Planning
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 14
Passenger k
Plan Valuation & Selection
Dec-MCTS
(Best et al. 2020)
Local Candidate Plans
Neighboring Robots
Decentralized Planning with Decentralized Monte Carlo Tree Search (Dec-MCTS)
Intro.
Contrib. 1
Contrib. 2
Summary
Notes: TODO (opt.) discuss planning distribution

## Slide 15
Centralized Planning with Simulation-Biased Randomized Variable Neighborhood Search (Sim-BRVNS)
Mothership
Centralized Solver
(Sim-BRVNS [X])
Mothership
Sim-BRVNS
(Panadero et al. 2023)
Intro.
Contrib. 1
Contrib. 2
Summary
Joint solutions

## Slide 16
Passenger k
Plan Valuation & Selection
Dec-MCTS
Candidate Plans
Neighboring Robots
Hybrid Framework
Stored Plans
Mothership
SimBRVNS
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 17
Evaluation in Simulated Ocean Domain
Tasks (T)
Mothership Location (M)
Deployed Passengers
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 18
Experimental Results
Initial (centralized) solution -> immediate coordination boost
Mothership-assisted replanning -> greater resilience to disturbances
Algorithms evaluated:
Initial, centralized solution only
Decentralized planning only
6 Robots, 20 Tasks
Initial + decentralized replanning
Initial + hybrid replanning
Task Completion Rate (Higher is better)
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 19
Contribution 1 Conclusions
Introduced Stochastic Multiagent Orienteering Problem
Explored leveraging mothership for hybrid decentralized problem solving
Evaluated scenarios where integrated mothership provides greatest benefits
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 20: Contribution 1 Publications
N. Butler and G. Hollinger, “ Hybrid Decentralization for Multi-Robot Orienteering with Mothership-Passenger Systems ,” in Proc. of the 42nd IEEE International Conference on Robotics and Automation, Atlanta, GA, May 2025.
N. Butler, G. Hollinger, J. Garwood, Y. Si, and A. Stewart, “Pseudo-Centralized Mission Planning for Under-Ice Robotic MOTHERSHIPs” [Poster]. 2nd Northwest Robotics Symposium, Corvallis, OR, April 2024.
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 21: Learning-Based Coordination for Passenger Robots in Complex Task Domains
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 22: Multi-Robot Coordination for Complex Tasks
Completing tasks may require robots to take adaptive, coordinated actions.
Intro.
Contrib. 1
Contrib. 2
Summary
Mothership
T
Communication relay behaviors
Exploration & discovery
Mothership
T
Notes: Real world sees complex tasks that may require multi-robot coordination.
Could discuss IvP Helm here

## Slide 23
How can we coordinate and adapt multi-robot behaviors to complete complex tasks in dynamic, comms-constrained environments using a Mothership-Passenger system?
Intro.
Contrib. 1
Contrib. 2
Summary
Notes: How can we coordinate, and adapt multi-robot roles for dynamic, low-comms environments using a Mothership-Passenger system?

## Slide 24: Mothership-Coordinated Adaptive Passenger Specializations (MCAPS)
Goals:
Maintain Passengers’ autonomy for quick, flexible response to environmental dynamics
Allow Mothership to influence each Passenger’s individual planning objectives such that resulting team performance is optimized
Intro.
Contrib. 1
Contrib. 2
Summary
Notes: Let’s try taking advantage of some domain knowledge without intensive, rigid behavior engineering (Maybe not include: or complex reward functions)?

## Slide 25: Passenger Candidate Objective Functions
Provide each Passenger with a set of domain-inspired objectives
Intro.
Contrib. 1
Contrib. 2
Summary
Apply domain knowledge without extensively engineered objective functions.
T
Mothership
Notes: Let’s try taking advantage of some domain knowledge without intensive, rigid behavior engineering (Maybe not include: or complex reward functions)?

## Slide 26: Globally-Aligned Behaviors
Intro.
Contrib. 1
Contrib. 2
Summary
Do Tasks
Relay Comms
Robot i Priorities
Tasks only
Comms only
Mixed
Do Tasks
Relay Comms
Robot j Priorities
Do Tasks
Relay Comms
Robot k Priorities
Joint priorities (specializations) produce team behaviors that maximize performance.

## Slide 27: Emergent Behaviors with Reinforcement Learning
Allow the Mothership to learn joint specializations that optimize team performance for different environment states
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 28: Mothership-Coordinated Adaptive Passenger Specializations (MCAPS)
Intro.
Contrib. 1
Contrib. 2
Summary
Notes: Let’s try taking advantage of some domain knowledge without intensive, rigid behavior engineering (Maybe not include: or complex reward functions)?

## Slide 29: MCAPS contd.
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 30: Training the Coordination Policy
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 31: Simulation Environment
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 32: Training Evaluation – Specialization Adaptation
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 33: Evaluations Against Hybrid-Decentralized & Heuristics
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 34: Evaluations Discussion?
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 35: Hardware Trials
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 36: Greedy vs Coordinated Hardware Deployments
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 37: Hardware Discussion?
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 38: Contribution 2 Conclusions
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 39: Conclusions
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 40: Thesis Summary
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 41: Thesis Contributions
Intro.
Contrib. 1
Contrib. 2
Summary
Notes: Merge with outline?

## Slide 42: Future Work
Intro.
Contrib. 1
Contrib. 2
Summary

## Slide 43
Contact:
Nathan Butler: butlnath@oregonstate.edu
Dr. Geoffrey Hollinger: geoff.hollinger@oregonstate.edu
NSF Award No.
2322055
TODO: List committee

## Slide 44: Image References
TODO: How to best do these in slides?
[1] Larter, Robert, Basal Melting, Roughness and Structural Integrity of Ice Shelves. Geophysical Research Letters. Volume 49, 202 10.1029/2021GL097421.
[2] M. Modasshir, S. Rahman, O. Youngquist and I. Rekleitis, Coral Identification and Counting with an Autonomous Underwater Vehicle, 2018 IEEE International Conference on Robotics and Biomimetics (ROBIO), Kuala Lumpur, Malaysia, 2018, pp. 524-529, doi: 10.1109/ROBIO.2018.8664785.
[3] S. MahmoudZadeh and A. Yazdani, Distributed task allocation and mission planning of AUVs for persistent underwater ecological monitoring and preservation, Ocean Engineering, Volume 290, 2023

## Slide 45: Marine Mothership-Passenger Platforms
MOOS-IvP + IvP Helm: Tends to treat Passengers only as executors, with no agency (no decentralized planning). IvP-Helm coordinates Passenger behaviors (rigid).
  Behaviors: ConstantDepth/Speed, AvoidObstacles, Loiter, Surface, Waypoint etc.
    These are not really planning-type behaviors that support mission-level coordination between robots
  Coordinating Multiple Autonomies to Improve Mission Performance adds “Neptune,” which is sort of a Mothership-like entity

## Slide 46: Marine Mothership-Passenger Platforms
Dynamic Mission Planning Framework for Collaborative Underwater Operations Using Behavior Trees: plans missions on Mothership, executes on Passengers (no replanning, limited adaptation/coordination)
Distributed task allocation and mission planning of AUVs for persistent underwater ecological monitoring and preservation
  Initially centralized (not necessarily on Mothership), then decentralized

## Slide 47: Gap
Most current methods favor centralized planning, decentralized execution (with minor adjustments). Not satisfactory for dynamic environments or long-range missions (must have greater decentralized autonomy).
So, how can we enhance decentralized autonomy with Mothership?
  (in ways that IvP Helm cannot? I guess IvP Helm doesn’t natively plan, just adapts behaviors according to external specs…)

## Slide 48: Decentralized, Role-Based Coordination
Maybe skip this slide
Intro.
Contrib. 1
Contrib. 2
Summary
Notes: Here are some methods (Focus on adaptability required alongside intermittent communication):